Town of Turtleford

Residential Fire Control Bylaw

Checklist

| Name of Resident: |  |
| --- | --- |
| Civic Address: |  |
| Legal Land Description: |  |

1.  Fire Pit

Width or Diameter: _________________________________________________

(must not exceed 75cm/29.52 inches)

Lining: ___________________________________________________________

(brick, stone, concrete)

- Covered with heavy gauge metal

Opening on screen: _________________________________________________

(not exceeding 13mm/0.5 inches)

Separated from grass or other vegetation: _______________________________

(at least 40cm/15.7 inches)

Separated with: ____________________________________________________

(clean earth, sand, gravel, or other non-combustible material)

2.   Location

(   Not located on balconies/wooden decks/combustible surfaces.

_____________________ from property line, building or combustible structure.

(no closer than 3 meters/9.8 feet)

_________________________________ from neighboring residential dwellings.

(no closer than 6 meters/19.685 feet)

3.    Diagram

4.    APPROVED

- Yes

- No

Comments: ________________________________________________________

__________________________________________________________________

__________________________________________________________________

__________________________________________________________________

Inspected by: ____________________________________

Date: __________________________________________

BYLAW NO. 285/05

PART 3 – REGULATIONS

- No owner shall light, ignite, start or allow to be light, ignited or started, any fire in a fire pit or cheminea without first obtaining an inspection by the Firechief or other officer-in-charge.

- No fire pit or chemineas shall be allowed to be used between the hours of 12:00 midnight and 9:00 a.m.

- No material or fuel other than seasoned wood, propane, natural gas or other town approved material or fuel may be burned in a fire pit, indoor wood burner, cheminea or fireplace in a residential zone.

- No owner shall leave a fire unattended.

- Fire pits may not exceed seventy-five (75) centimeters (29.52 inches) in width or diameter and must be lined with brick, stone, or concrete.

- The brick, stone or concrete in a fire pit or any chemineas shall be separated from grass and other vegetation by a distance of at least forty (40) centimeters (15.7 inches) by means of clean earth, sand, gravel or other non-combustible material.

- All fire pits or chemineas openings must be covered with heavy gauge metal screen with openings not exceeding 13 millimeters (0.5 inches)

- No fire pit or chemineas may be located closer than three (3) meters (9.8 feet) from any property line, building or other combustible structure any may not be closer than six (6) meters (19.685 feet) from any neighboring or abutting residential dwelling.

- Chemineas shall not be used on balconies, wooden decks or any combustible surface.

- If smoke from an open-air fire causes an unreasonable interference with the use and enjoyment of other person’s property, and a complaint is received, the Firechief or Deputy Firechief may request that the fire be extinguished immediately.

- The Council of the Town of Turtleford reserves the right by resolution to ban the use of fire pits or chemineas on a specific lot or parcel of land if the Town Administrator receives written complaints about the fire pit or chemineas form the abutting property owners or tenants.

# Text boxes

neighboring property

garage

19.7 feet

9.8    feet

house

9.8    feet

19.7 feet